# Spotlights on Case IH solutions for the sugar cane industry at SIMA 2015

Close to customers with competence, tradition and innovations: Case IH premiered the upgraded Austoft® 8000 Series

A special event for corporate customers from Africa and the Middle East operating in the sugar cane industry / Being close to customers is a top priority for Case IH / The upgraded Austoft® 8000 Series further improves the outstanding efficiency of these world renowned sugar cane harvesters

St. Valentin, 4 March 2015

Case IH’s latest generation of powerful agricultural equipment solutions for the sugar cane industry took centre stage at SIMA, the International Agri-Business Show held from 22 to 26 February 2015 in Paris Nord Villepinte, France.

“Exceeding our customers' expectations in terms of productivity and profitability and supporting them with innovative products and excellent services is our mission,” said Mathew Foster, Case IH Vice President and responsible for Europe, Africa and the Middle East, during a special event organized by Case IH on the opening day of the show. The event was attended by more than 40 dealers and representatives of corporate customers and large agro-industrial farms operating in the sugar cane and bio-ethanol sectors from African and Middle Eastern countries, including Sudan, Mozambique, Tanzania, Kenya, Zimbabwe, Nigeria and Sierra Leone. “With new product launches in 2015, we intend to further strengthen our company’s position as a full-liner of agricultural equipment for our existing and future customers in Africa and the Middle East,” added Foster.

After his welcome speech, participants were provided with insights on the latest Case IH innovations, which include the Austoft® 8000 Series of industry-leading sugar cane harvesters and the high-horsepower tractors, well represented by the MagnumTM and PumaTM units on display. Two walk-around presentations were given by Yoann Clarisse and Patrice Loiseleur, respectively Case IH Harvesters Product Specialist EMEA and Case IH International Agriculture Projects and Corporate Farming Manager.

“Being close to our customers is a main priority for us, and dealers play a key role to build customer satisfaction. That’s why we are committed to creating the industry’s most professional dealer network to meet the demanding requests from our customers.” highlighted Foster. Case IH is able to provide not only first-class agricultural machinery but also qualified knowledge and a full range of services, including extensive after-sales support, and technical training to support the long term growth of its customers’ businesses. “We are also making a huge investment to bring our sugar cane parts supply system to Europe in order to shorten delivery times and better support our African and Middle Eastern customers.

“To further support our network and strengthen our presence in Africa and the Middle East, this year we are creating a dedicated Case IH team for this region to support its huge potential for growth, with particular attention to corporate farming,” added Foster.

As evidence of Case IH’s attention to this specific customer segment, the company displayed the newly upgraded Austoft 8000 sugar cane harvester which attracted lively interest from visitors. “Sugarcane is one of the fastest-growing crops in terms of land area worldwide,” concluded Foster. “By presenting the upgraded Austoft 8000 Series with fully integrated AFS solutions for precision farming, we confirmed our company as a leading global provider of innovative harvesting solutions for all crop types.”

An unparalleled history in sugar cane harvesting

Austoft has been a renowned brand in sugar cane harvesting since 1941 and market leader in alcohol and sugar industries for more than 30 years. The Case IH Austoft A8000 wheeled version and the A8800 series on tracks are high performance sugar cane harvesters designed for high productivity levels and the lowest total cost of ownership; they are auto guidance and telematics ready, offer Can Bus systems, intelligent engine rpm adjustment, and low centre of gravity which is perfect for hilly conditions. These machines are easy and comfortable to operate and maintain with the longest 600hrs engine oil change intervals and show the lowest levels of soil compaction.

Fuel efficient and powerful FPT Cursor 9 engine

The 9 litre FPT Cursor 9 engine, a water cooled 6 cylinder power pack with turbo charger and after cooler, delivers up to 394 hp. “1,800erpm during regular operation leaves power for demanding harvesting conditions whilst Smart Cruise technology reduces fuel consumption to 0.7 litre of fuel per tonne of cane billet. These engines are available with a choice of emission standards on demand. The engine compartment is pressurised, leaving the engine clean at all times to prevent the risk of fire in hot and dry harvesting conditions. With a logically directed and electronically reversible air flow, the highly efficient cooling package is designed for working temperatures up to 55°C. The cooling system includes an efficient self-cleaning device, and the air flow is adapted to the prevailing cooling demand”, said Clarisse who conducted the product presentation.

New high-throughput chopper

“The new chopper is at the core of the A8000 and A8800 series”, emphasised Clarisse. “With a 40 US gallons/min oil flow increase and a chopper speed up to 205 rpm, the new A8000 series delivers more chopping power and a 20% increase in throughput. In addition, using equally simple and reliable hydraulic components and improved throwers in the choppers helps to reduce downtime and maintenance requirements, thus further adding to the already excellent return on investment of this machine”, said Yoann Clarisse.

With a 45º angle and a new rotating and removable toe, the crop divider is yet another exclusive Case IH feature. “Operators will experience better performance in lifting recumbent cane with less soil movement and mineral impurities. The slip-on shoes, which are available as DIA kit, are shorter and lighter and offer easy maintenance. The optional rotating side knife with hydro adjustment reduces downtime by avoiding any blockage with trash and weeds. The A8000 and A8800 series are equipped with auxiliary or outer dividers as standard and provide markedly higher efficiency in entangled canes”, explains Clarisse. Toppers are either available in a standard version or as optional shredder topper.

For higher capacity and throughput, the three blade heavy duty Case IH 15’’ rotors are powered by two hydraulic motors and two shafts through direct couplings. “That is just one of the decisive differences when comparing our harvesters with competing machinery – where just one motor is used”, highlights Yoann Clarisse.

Exclusive Case IH Anti-vortex cleaning system: Efficient innovation in cane harvesting

The exclusive Anti-vortex system designed by Case IH has proven to be the most modern and efficient cleaning system. In addition to reducing the amount of extraneous matter and cane loss, this system improves the load density for transport, thus achieving lower operating costs. Designed to increase airflow in the primary extractor chamber, the system was tested in countries like Reunion and Mauritius with most productive cane varieties.

The extractor fan is driven hydraulically via a vertical shaft mounted in a two-piece, high-density plastic hood. The main purpose is the separation of trash from cane billets and the deposition of trash in a controlled flow behind the machine. The fan operates at 850rpm, compared to 1,300rpm of traditional systems, providing a 22.4 kW reduction of power requirement and increased fuel efficiency. The Anti-vortex system reduces the percentage of trash (leaves and stems) by around 20% compared to other systems, cane losses from 176 kg/ton to 4.8 kg/ton, and net sugar losses accordingly (+/- 2% per ha). In addition, Case IH is the first manufacturer to offer yield monitoring capabilities. The system will be available on the 2015 models, enabling operators to monitor cane yield and trash ratio as well as net sugar production per square metre.

Comfortable cab, high precision

“Case IH A8000 and A8800 sugar cane harvesters offer operational comfort that is best in class”, says Yoann Clarisse. “In these cabs, operators enjoy optimum ergonomics, excellent visibility with a 180° angle vision from the seat, the AFS 700 touch screen display and the intelligent Eco Power cruise system as standard. In addition, these machines comes auto guidance and telematics ready and offer either joystick control for higher manoeuvrability or the optional steering wheel. For high comfort during long working hours, the cabs also feature four point cab suspension”, explains Clarisse.

Case IH A8000 and A8800 series sugar cane harvesters can easily be equipped with Telematics – so customers instantly see the current status of their machines. “Knowing at an instant if the machine is stopped, idling, or working will increase overall efficiency and thus gain valuable harvesting hours”, says Yoann Clarisse.

AutoTracker – the tool to effectively reduce cane losses – exclusive to Case IH

The exclusive, factory-fitted AutoTracker helps to minimise cane losses. Cane stalks are cut at ground level, and the base cutter height is either controlled by the operator or automatically by the AutoTracker which consists of two rotating discs with 5 blades each. The cutter angle can be adjusted from 12,5º to 17,5º. On average, the AutoTracker reduces stool damage by 27.2%, root ripping at the end of rows by 28.3%, and the overall cane losses by an impressive 62.9%”, emphasises Yoann Clarisse. “Independent trials have indicated a reduction of cane loss of approximately 720 kg/ha. By avoiding ground contact by the base cutter disc, the AutoTracker ensures excellent work quality on any type of terrain, including sandy and loose soils. That is particularly true in cane crops that are being harvested for the first time – and that clearly means less stress and fatigue for the operator”, adds Clarisse.

Case IH A8000 and A8800 key features:

# Tracked and wheeled models available

# Radial Tyres for wheeled version

# Efficient FPT Cursor 9 engine with Tier III or Tier 0 and Tier 4B emission standards on demand

# New chopper with 39% more chopping power

# Throughput increased by 20% – efficiency increased by one fifth

# Simple and reliable hydraulic components effectively reduce downtime

# Auxiliary or outer dividers as standard provide markedly higher efficiency in entangled canes

# 3 or 4 blade heavy duty Case IH 15’’ rotors powered by two hydraulic motors and two shafts

# Exclusive Case IH primary Anti-vortex extractor

# Comfortable cab with optimum ergonomics, excellent visibility

# Auto guidance and telematics ready as standard

# Overall cane losses reduced by 62.9%

***

Press releases and photos http://mediacentre.caseiheurope.com/.

Case IH is the professionals' choice, drawing on more than 170 years of heritage and experience in the agricultural industry. A powerful range of tractors, combines and balers supported by a global network of highly professional dealers dedicated to providing our customers with the superior support and performance solutions required to be productive and effective in the 21st century. More information on Case IH products and services can be found online at www.caseih.com.

Case IH is a brand of CNH Industrial N.V., a World leader in Capital Goods listed on the New York Stock Exchange (NYSE: CNHI) and on the Mercato Telematico Azionario of the Borsa Italiana (MI: CNHI). More information about CNH Industrial can be found online at www.cnhindustrial.com.

For more information contact:

Cecilia Rathje

Ph: +43 7435 500 634

Case IH Public Relations Officer

Europe, Middle East & Africa

Email: cecilia.rathje@cnhind.com

www.caseih.com

Reprint free of charge, copy requested!