Case IH extends popular Puma line of tractors with two higher-horsepower ROPS models

New Puma 155 ROPS and 185 ROPS introduced to Middle East and African markets in response to customer demand

St. Valentin, 14 November 2017

Case IH has added two new models to its popular Puma tractor line, the Puma 155 ROPS (with a maximum output of 161hp) and the Puma 185 ROPS (producing a maximum of 197hp). Both vehicles are being introduced in response to demand for more powerful tractors with an open deck, a canopy, and a rollover protective structure (ROPS).

Christian Ramnek, Case IH Middle East & Africa Product Marketing Specialist Tractors, said: “These two new Puma models are ideal for farmers who need multipurpose tractors in the medium horsepower range and a perfect balance between power and weight. Just as with the well-established Puma cab models, they are capable of performing light and heavy tasks in a wide range of applications. We expect to see these tractors go into service in haulage, cultivation, seeding, crop protection, and heavy draft operations. They are also useful for stationary work such as driving water pumps, generators, wood-choppers, hammer mills and other applications.”

Beneath the familiar Puma hood with its shark-fin air inlets, each new tractor is equipped with a 6.75-litre six-cylinder engine with mechanical fuel injection. Combustion is enhanced by a turbocharger with an air-to air intercooler which cools the compressed air to increase its density. Power output is complemented by 690 Nm of torque at 1,400 rpm in the Puma 155 ROPS and 760 Nm of torque at 1,400 rpm in the Puma 185 ROPS.

The FPT Industrial engine drives through a 15x12 synchronized mechanical transmission designed for minimal power losses. This provides a mechanical shuttle shift (forward/reverse) and nine speeds in the main working range of 4-12 km/h (maximum speed is 30 km/h). An optional creeper gear offers 30x24 speeds and a minimum working speed of 0.4 km/h at 2,200 rpm. For mechanically driven implements the PTO (power take off) system offers two speeds at 540 and 1,000 rpm.

Both new Puma models can efficiently operate large hydraulic implements, with an oil delivery rate of 110 litres/minute at rated engine speed and system pressure of up to 215 bar. With a powerful three-point linkage with a real lift capacity of 6,475 kg through the whole lift range, even the biggest implements can be operated. Case IH’s renowned Lift-O-Matic™ quick-raise system ensures easy and accurate setting of implement lift height and work position as well as quick, comfortable headland turns.

Axle capacity of both new tractors is 4,200 kg at the front and 6,300 kg at the rear, with the option of a 112-inch bar axle for dual rear wheels. A wide-track version, with track setting up to three meters, is also available for special row-spacing applications.

To enable long working days without unwanted interruptions for refueling, the Puma 155 ROPS and 185 ROPS can have a generous fuel tank capacity of 395 litres, attained with a 290-litre main tank and an optional 105-litre supplementary tank. So that only clean fuel is used, a dual-cartridge fuel filter is standard, as is a water separator to protect the fuel pump injection system.

Daniel Bordabossana, Case IH Marketing Manager Africa & Middle East, commented: “Puma tractors are well-established in this region, with a hard-earned reputation for affordability, high-quality engineering, ease of operation, and efficiency. By introducing two new ROPS tractors with higher horsepower, we now offer a wider range of tractors to satisfy customer demand, providing farmers with exactly what they tell us they need.”

***

Press releases and photos http://mediacentre.caseiheurope.com/.

Case IH is the professionals' choice, drawing on 175 years of heritage and experience in the agricultural industry. A powerful range of tractors, combines and balers is supported by a global network of highly professional dealers dedicated to providing our customers with the superior support and performance solutions required to be productive and effective in the 21st century. More information on Case IH products and services can be found online at www.caseih.com.

Case IH is a brand of CNH Industrial N.V., a world leader in capital goods listed on the New York Stock Exchange (NYSE: CNHI) and on the Mercato Telematico Azionario of the Borsa Italiana (MI: CNHI). More information about CNH Industrial can be found online at www.cnhindustrial.com.

Case IH Media Center

www.caseih.com

www.facebook.com

www.youtube.com

For more information contact:

Silvia Kaltofen

Ph: +43 7435 500 652

Case IH Communication Specialist Africa & Middle East

Email: silvia.kaltofen@cnhind.com